## Slide 1: HEAT ENERGY CONVERSION PROCESSES
Direct Thermoelectric Conversion
Engine Conversion of Solar Energy
Heat Pumps
Geothermal and Ocean-thermal Conversion

## Slide 2: Direct Thermoelectric Conversion
Thermoelectric Generators
Thermionic Generators

## Slide 3: 1. Introduction
Thermoelectricity refers to a class of phenomena in which a temperature difference creates an electric potential
or an electric potential creates a temperature
difference.
Thermoelectric power generator is a device that
converts the heat energy into electrical energy based on the principles of Seebeck effect
The pioneer in thermoelectric was a German scientist Thomas Johann Seebeck (1770-1831)
Later,
In 1834, French scientist,
Peltier and in 1851,
Thomson (later Lord Kelvin) described the thermal effects on conductors

## Slide 4: 2. Seebeck, Peltier and Thomson effect
Seebeck effect
When the junctions of two different metals are maintained at different temperature, the emf is produced in the circuit. This is known as Seebeck effect.
The conductor 1 is maintained at T+∆T temperature
The conductor 2 is maintained at
temperature ‘T’.
Since the junctions are maintained at different temperature, the emf ‘U’ flows across the circuit.

## Slide 6: Peltier effect
passes through
the circuit of two dissimilar
Whenever current conductors, depending
on the current direction, either heat is
released
absorbed or released at the junction of the two conductors. This is known as Peltier effect.
absorbed

## Slide 8
Thomson effect
Heat is absorbed or produced when current flows in material with a certain temperature gradient. The heat is proportional to both the electric current and the temperature gradient. This is known as Thomson effect.
3. Thermoelectric effect
The thermoelectric effect, is the direct conversion of heat differentials to electric voltage and vice versa

## Slide 9: 4. Thermoelectric materials
The good thermoelectric materials should possess
  Large Seebeck coefficients
  High electrical conductivity
  Low thermal conductivity
The example for thermoelectric materials
  BismuthTelluride (Bi2Te3),
  Lead Telluride (PbTe),
  SiliconGermanium (SiGe),
  Bismuth-Antimony (Bi-Sb)

## Slide 10: 5. Principle, construction and working of Thermoelectric power generator
Heat input
Hot junction
Cold junction
P-type
N-type
Heat ejection
Power output
Thermoelectric power generator based on the principle of Seebeck effect that when the junctions of two different metals are maintained at different temperature, the emf is produced in the circuit

## Slide 11
In order to select materials and design a thermoelectric generator, one needs to start with a general understanding of the thermoelectric effects.
In a thermoelectric material there are free carriers which carry both charge and heat.
Perhaps the simplest example is a gas of charged particles.
If a gas is placed in a box within a temperature gradient, where one side is cold and the other is hot, the gas molecules at the hot end will move faster than those at the cold end.
The faster hot molecules will diffuse further than the cold molecules and so there will be a net build up of molecules (higher density) at the cold end.
The density gradient will cause the molecules to diffuse back to the hot end.

## Slide 12
In the steady state, the effect of the density gradient will exactly counteract the effect of the temperature gradient so there is no net
flow of molecules.
If the molecules are charged, the buildup of charge at the cold end will also produce a repulsive electrostatic force (and therefore electric potential) to push the charges back to the hot end.
Diagram shows
The charge buildup at cold side

## Slide 13
The electric potential produced by a temperature
difference is known as the Seebeck effect
and the
Seebeck
proportionality constant is called the coefficient.
If the free charges are positive (the material is p-type),
will build up on the cold which will
positive charge have a
positive potential.
Similarly, negative
free charges (n-type material) will
produce a negative potential at the cold end.

## Slide 14: Construction Thermoelectric power generation (TEG) devices typically use special semiconductor materials, which are optimized for the Seebeck effect.
The simplest thermoelectric power generator consists of a thermocouple, comprising a p-type and n-type material connected electrically in series and thermally in parallel.
Heat is applied into one side of the couple and rejected from the opposite side.
An electrical current is produced, proportional to the temperature
gradient between the hot and cold junctions.

## Slide 15: Therefore, for any TEPG, there are four basic component required such as
Heat source (fuel)
P and N type semiconductor stack (TE module)
Heat sink (cold side)
Electrical load (output voltage)

## Slide 16
The figure shows the construction of thermoelectric
power generator.
There is a burner in which the propane fuel is used as heating source in one side.
The exhaust is used to transmit a burnt fuel.
On the other side, a cold junction is kept.
The thermoelectric module (TE) (consist of number of
P- type and N-type semiconductor pellets connected in
series or between
parallel depending on the served load)) is kept in the hot and cold junction.
The electrical out (load) is taken from the TE module.

## Slide 17: Working
When the two sides of semiconductor are maintained with different temperature, the emf is flows across the output circuit
N-type
Cold side
Hot side
Heat flow
V
Electron flow

## Slide 18
charge hence
As the heat moves from hot side to cold side, the carrier moves in the semiconductor materials and the potential deference is created.
The electrons are the charge carriers in the case of N- type semiconductor and Hole are in P-type semiconductors.
In a stack, number of P-type and N-type
voltage
semiconductors is connected.
A single PN connection can produce a Seebeck of 40 mV.
The heat source such as natural gas or propane are
used for remote power generation

## Slide 19: Major Types available
Fossil fuel generators
Solar Source generators
Nuclear Fuel generators

## Slide 20: Advantages
Easy maintenance: They works electrically without any moving parts so they are virtually maintenance free.
•
Environment friendly: Thermoelectric
generators
produce no pollution. Therefore they are eco friendly
generators.
Compact and less weight: The overall thermoelectric
cooling system is much smaller and lighter than a comparable mechanical system.
High Reliability: Thermoelectric modules exhibit very
high reliability due to their solid-state construction

## Slide 21
No noise: They can be used in any orientation and in zero gravity environments. Thus they are popular in many aerospace applications.
Convenient Power Supply: They operate directly from a DC power source.

## Slide 22: Applications

## Slide 23
TEG System
Load : LED lighting

## Slide 26: THERMIONIC

## Slide 27: Introduction
Thermionic Power Convertor is a static device that converts heat into electricity by boiling electrons from a hot emitter surface(approx 1800 K) across a small inter electrode gap(<
0.5 mm) to a cooler collector surface(approx 1000 K)
A Thermionic Generator consists of one or more of these convertors coupled to give desired power output
Thermionic generators can be operated from any primary heat source.
For low power level(3 kW or less) solar energy can be used
For high power level (50 kW or more) nuclear heat source can
be used

## Slide 28: History
In 1883 Edision discovered release of electrons from a hot body
In 1904 Fleming invented thermionic diode rectifier
In 1915 Schlicter proposed thermionic conversion
After 1950 serious research on this began

## Slide 29: Common components

## Slide 30: Important aspects considered
The cathode must emit an abundant supply of electron
Evaporation of atoms from cathode should be negligible
Electronic space charge build-up in the inter- electrode spacing must be eliminated

## Slide 31: Classification
Classification according to methods of neutralization space charge
Vacuum close-spaced
Cesium Gas Filled

## Slide 32: Vacuum close-spaced convertor
Has been under extensive research since 1957
Physical spacing of .0005 inch or less is maintained between anode and cathode
Will have engineering difficulty
Lifetime is 40 hours

## Slide 33: Cesium Gas Filled
Cesium gas is filled between anode and cathode
Working efficiency is higher than former one
Lifetime is nearly 600 hours
Main problem is efficient sealing and corrosive nature of cesium

## Slide 34: Advantages
Rotating equipment is not employed
Liquid-Vapour phase problems do not exist
Separators for fluids are not required
Frictional losses due to bearings not present

## Slide 35: Disadvantage
Individual convertors are low voltage, high current devices
A large number of convertors must be sequentially arranged to obtain useful voltage
Power losses in convertors can seriously cut useful power output

## Slide 36: Application

## Slide 39: COMBINATION OF THERMIONIC AND THERMOELECTRIC

## Slide 40: Comparison
Both thermionic and thermoelectric generators employ the electron gas as the working fluid
A thermionic generator based on the ballistic current flow which is highly efficient, and its theoretical efficiency is close to the Carnot efficiency
A thermoelectric generator, however, has poor efficiency due to the diffusive current flow
A thermionic generator usually requires a high- temperature heat source (e.g. 1500 K) to generate a practically useful current
A thermoelectric generator, however, can produce electrical power from low-quality heat energy sources

## Slide 41: Combination

## Slide 43: THANK YOU