## Slide 1
Introduction to Biomass Energy Conversions

## Slide 2: Outline
1
2
Introduction
Biomass as Renewable Energy Resources
Bioenergy production overview
Biomass to energy routes
Energy conversion systems
Conversion Technologies
Thermochemical Processes
Biochemical Processes

## Slide 3: Introduction
Biomass as a renewable resource
Biomass is biological organic matter derived from living or recently-living organisms
Bioenergy is the energy contained (stored) in biomass
Biomass is an extremely important energy source, available nearly everywhere
Biomass encompasses a large variety of materials, including wood from various sources, agricultural and industrial residues, and animal and human waste
Two forms of biomass
Raw: forestry products, grasses, crops, animal manure, and aquatic products (seaweed)
Secondary: materials that undergone significant changes from raw biomass. Paper, cardboard, cotton, natural rubber
products, and used cooking oils.
4

## Slide 4: Introduction Biomass as a renewable resource
5
6

## Slide 5: How Biomass gets its energy
6

## Slide 6
Example of Bioethanol Production
7

## Slide 7: Bioenergy Production Overview
8
9

## Slide 8: Bioenergy
9
Bioenergy is the energy retrieved from biomass sources. It is the largest used renewable energy resource in the world
Large bioenergy potential: Biomass resource is widely available and diversified in the Kingdom: Livestock waste, Municipal and Industrial effluents (paper, plastic, food, …etc.), Poultry waste, Sewage sludge
Bioenergy is a significant mean for waste disposal to prevent environmental pollution and allow economic stability
Main Technologies:
  Biogas based power plant technology
  Gasification power plant technology
  Biodiesel and Bioethanol Plants technology

## Slide 9: Biomass provides more than 10 % of Global energy use (International Energy Agency, 2013)

## Slide 10: Bioenergy Production Routes
Biomass Feedstock
Thermoche mical Platform
Biochemical Platform
Chemical Platform
Combustion
Pyrolysis
Gasification
Anaerobic digestion
Fermentation
Trans- esterification
Combined heat & power, Fuels, Chemicals and materials
Heat
Char, Bio-oil Fuel gas
Fuel gases (Syngas, H2)
Biogas (methane)
Bioethanol
Biodiesel

## Slide 11
Pyrolysis products
Bio-oil
Char
Syngas
Bioethanol
13
14
Biodiesel

## Slide 12
15
Bio-Power generation of top 20 countries for 2010-2012
(International Energy Agency, 2012)

## Slide 13: Global Production of Bioethanol and Biodiesel (International Energy Agency, 2012)
16

## Slide 14: Energy generation systems
17

## Slide 15: Energy generation systems

## Slide 16
Energy generation systems
Steam turbine
19

## Slide 17
Energy generation systems
20
Combined heat & power system

## Slide 18: Biomass Energy Conversions Technologies 1- Thermochemical processes

## Slide 19: Thermochemical conversion options
22

## Slide 20: Pyrolysis
decomposition of solid
by heat in absence of
Thermal biomass oxygen
First step of in combustion and gasification processes
Biomass is converted into solid
charcoal, liquid (bio-oil) and gas
The process is endothermic
Because unavoidable system, a
some oxygen is in any pyrolysis small amount of
oxidation occurs
Dry Biomass € char + (CO, CO2, H2, H2O (g), CH4) + tars + Ash
22
23

## Slide 21: Pyrolysis
Classification of Pyrolysis methods
24

## Slide 22: Typical Pyrolysis results
-20 -10
0 10 20 30 40 50 60
70 80 90 100 110 120 130 140
Time [min.]
0
200
400
600
Temperature [ C]
furnace temperature
mean bed temperature
furnace heating
carbonization
cooling
o
charging
25
Temperature profile in standard Pyrolysis test
800

## Slide 23: Gasification
26
Conversion of solid biomass into combustible gas mixture called producer gas (CO + H2 + CH4)
in presence of limited (O2/air)
Involves partial combustion of biomass (controlled combustion)
Four distinct process in the gasifier
Basic Process Chemistry schematic

## Slide 24: Gasification
Producer Gas Characteristics
Component | Rice Husk | Woody Biomass
CO | 15-20% | 15-20%
H2 | 10-15% | 15-20%
CH4 | Upto 4% | Upto 3%
N2 | 45-55% | 45-50%
CO2 | 8-12% | 8-12%
Gas C.V. (kcal/Nm3) | Above 1050 | Above 1100
Gas generated in Nm3/kg of biomass | 2 | 2.5

## Slide 25: Gasification
Classification of Gasification methods
Classification | Conditional factor
Gasification pressure | Normal pressure (0.1-0.12 MPa), High pressure (0.5- 2.5 MPa)
Gasification temperature | Low (< 700 °C), High (> 700 °), High temperature decomposition (> ash fusion point)
Gasification agent | Air, oxygen, steam and combination of them, carbon dioxide for particular time
Heating (temperature zone formation) | Direct (heat generation from reaction of partial gasification raw material and oxygen) Indirect (external heat)
Gasifier types | Fixed bed, flow-bed, circulating flow bed, entrained bed, mixing bed, rotary kiln, twin tower, molten furnace

## Slide 26: Gasifier types
29
Updraft Gasifier
+ Suitable for moderate outputs [2-12 MWe]
+ Good fuel flexibility [fines, small & large chips]
+ Good turndown
Low gas quality
Very high tars [100g/nm3] – requires extensive secondary tar cracking with catalysts [Ni based or
dolomite]
High capital cost

## Slide 27: Gasifier types
30
Downdraft Gasifier
+ Very low tar gas [< 1 g/nm3]
+ Good gas CV [~5 MJ/nm3]
+ Simple gas train possible
+ Modular design
+ Simple construction and operation
Limited scalability [0.5 MWe~ 500 kg/h]
Precise fuel requirements [size, shape, moisture]
Engine costs can be high relative to other costs
Limited turndown

## Slide 28: Gasifier types
31
Twin-fire Gasifier
+ Suitable for large electrical outputs [> 5- 10 MWe]
+ More flexible in use of steam, air, steam/O2 mix
+ High gas CV – 8-12 MJ/nm3
+ High overall electrical efficiencies [gas turbine use]
Complex design
Limited turndown
Stable operation difficult [DPs, gas flows]
High tar levels in gas – extensive cleaning/catalytic cracking required [Ni based
or dolomites].
Feed pretreatment to small particles

## Slide 29: Gasifier types
32
Crossdraft Gasifier
+ Operable at very small scale (10kW and below)
  Minimum tar conversion capabilitites
  High exit gas velocity and temperature

## Slide 30: Gasification Technology scale output
33

## Slide 31: Example of gasification unit in UK
34

## Slide 32: Biomass Energy Conversions Technologies 2- Biochemical processes

## Slide 33
Anaerobic Digestion
AD is a series of biological processes in which microorganisms breakdown biodegradable material in the absence of oxygen
End product of the process:
Biogas: a mixture of CH4 and CO2 mainly which is combusted to generate electricity and/or heat or processed into renewable natural gas and transportation fuel
Digested solid: residue from the digester, can be composted and applied as land amendment or used for dairy bedding
Nutrients: residue from liquid digestate, used in agriculture as fertilizer
Various feedstock can be used:
Livestock manure, municipal wastewater solids, food waste, industrial wastewater and residuals, fats, and other organic waste streams

## Slide 34: Anaerobic Digestion Principle
Initial hydrolysis of particulate matter and larger molecules
Fermentation (acidogenesis) (formation of acids) generating primarily acetate but also other Volatile Fatty Acids (VFA)
Acetogenesis (formation of acetate), Hydrogen is used as an electron acceptor
Methanogenesis Acetate € CO2+ CH4 (major pathway app. 70%) 4H2 + CO2 € CH4 + 2H2O
37

## Slide 35: Anaerobic Digestion
Parameters | Optimal conditions
Total solid content (TS) | Low (<10 %) Medium (10-20 %) High (20-40%)
Temperature | Mesophilic (20-45 °C) Thermophilic (50-65 °C)
Retention time | 15-30 days for mesophilic 12-14 days for thermophilic
pH | Optimum between 6 – 7 Low pH inhibit acidogenesis stage High pH is toxic for methane forming bacteria
Carbon to Nitrogen ratio (C:N) | Optimum between 20 – 30 High C:N € rapid N consumption € lower gas production Low C:N € ammonia accumulation € toxicity
Organic loading rate (OLR) | High OLR € accumulation of inhibiting substances € low biogas yield
38
Parameters and conditions influencing AD

## Slide 36: Anaerobic Digestion
Effect of operating temperature
39

## Slide 37: Anaerobic Digestion
Type of biomass | Biogas yield [m3/t]
Beef slurry | 25
Dairy waste | 55
Cuttings from beet | 75
Green waste | 110
Biowaste | 120
Fresh fat | 400
Old fat | 800
40
Biogas properties
Biogas potential of some biomass substrate

## Slide 38: Anaerobic Digestion
Biogas properties
41

## Slide 39: Anaerobic Digestion
42
Typical Biogas Power Plant

## Slide 40: Anaerobic Digestion
43
Schematic of a typical agricultural AD system

## Slide 41
44

## Slide 42: Anaerobic Digestion
45

## Slide 43: Anaerobic Digestion
1 toe = 11.63 MWh
46
Biogas Production at 2012 and trend to 2022 (Pike Research, 2012)

## Slide 44: Fermentation
47
Bioethanol production process

## Slide 45: Fermentation
48
Bioethanol production flow diagram
Feedstock: corn, wheat, sugarcane, rice, potato, …

## Slide 46: Conclusion
Biomass is a sustainable and reliable energy resource
The growth rate of biomass energy use is about 1 % each year
Technological barriers have to be overcame in order to promote the bioenergy development:
  Upgrading the bio-fuel quality by extracting harmful species especially for biogas and syngas (ammonium, sulfur compounds, silicon based compounds, particulate, …)
  Enhance the reaction mechanism for both AD and gasification processes